## Slide 1
Lesson no 7
Radar
Jamming

## Slide 2
CONTENTS
01. Pulse Radar System
02. Continuous Wave Radar
03. Pulse Doppler Radar
05. Radar jamming
04. Monopulse Radar

## Slide 3
01. Pulse Radar System

## Slide 4
The name describes a process of transmitting discrete bursts of RF energy at the frequency
of the radar system.
The time that pulses are transmitted determines the pulse repetition frequency (PRF) of the radar system.

## Slide 8
02. Continuous Wave Radar

## Slide 9
A continuous radar transmission from the antenna requires that classic CW radars have two antennas, one for transmission and one for reception.
The Doppler principle deals with the fact that a radar return from a moving target will be shifted in frequency by an amount proportional to its radial velocity relative to the radar site.

## Slide 12
03. Pulse Doppler Radar

## Slide 13
Pulse Doppler radars combine the advantages of both pulse and Doppler radar systems.
The beauty of a pulse Doppler radar is that it eliminates ground clutter and provides range, azimuth, and velocity resolution.

## Slide 16
04. Monopulse Radar

## Slide 17
Monopulse radars were developed to overcome the limitations and jamming susceptibility of scanning radar systems.
A monopulse radar typically receives returned radar energy in two or four separate receivers, or channels, each looking at a different area.
By comparing the returns from each receiver, track errors can be determined.

## Slide 21
05. Radar jamming

## Slide 22
Radar jamming is the intentional radiation or reradiation of radio frequency (RF) signals to interfere with the operation of a radar by saturating its receiver with false targets or false target information.
There are two types of radar jamming:
noise and deception.

## Slide 23
Noise Jamming
Noise jamming is produced by modulating a RF carrier wave with noise, or random amplitude changes, and transmitting that wave at the victim's radar frequency.

## Slide 24
Deception Jamming
Deception jamming uses complex receiving and transmitting circuits to process and retransmit jamming pulses that appear as a real target to the victim radar. A deception jammer receives the signal from the victim radar and alters the signal to provide false range, azimuth, or velocity information.

## Slide 25
False Target Jamming

## Slide 26
Impart of Noise Jamming

## Slide 27
Barrage Jamming

## Slide 28
Spot Jamming

## Slide 29
Spot Jamming Effectiveness

## Slide 30
False target

## Slide 31
Thanks